## Slide 1: OPTIMUM SELECTION OF STORAGE BATTERY FOR ELECTRIC VEHICLES USING MULTI CRITERIA DECISION MAKING TECHNIQUES
Group No: B-6
Presented by:
Anandu A
Aswanth Lal
Nihal Rashid
Muhammed Sinan Iqbal
DEPARTMENT OF MECHANICAL ENGINEERING
LBS COLLEGE OF ENGINEERING
KASARAGOD
Under the guidance of
Dr. Anil Kumar B.C

## Slide 2: OVERVIEW
Introduction
Objective
Literature Survey
Methodology
Result and Discussion
Conclusion
References

## Slide 3: INTRODUCTION
ELECTRIC VEHICLES (EV)
Uses electric motors for propulsion.
Important parts:
  Controller
  Battery
  Electric motor
Types of EV:
  Battery EV (BEV)
  Hybrid EV (HEV)
  Plug-in HEV (PHEV)

## Slide 4
Merits of EV
No Emission
Energy source is renewable.
Lower maintenance.
High efficiency.
Demerits of EV
Higher purchase cost.
Low speed and range.
Higher maintenance cost.
Slow charging.

## Slide 5: Battery Alternatives
Lithium Ion Phosphate (LFP)
Nickel Metal Hydride (NiMH)
Lithium Titanate Oxide (LTO)
Sodium Metal Halide (ZEBRA)
Lithium Manganese Oxide (LMO)
Lithium Cobalt Oxide (LCO)
Nickel Cadmium (Ni-Cd)

## Slide 6: Battery Parameters
Nominal Voltage (V)
Specific Energy (Wh/kg)
Energy Density (Wh/L)
Specific Power (W/kg)
Energy Efficiency (%)
Life Cycle
Working Temperature (˚C)
Production Cost

## Slide 7: MCDM Techniques
Technique for order preference by similarity to ideal solution (TOPSIS)
Evaluation based on distance from average solution ( EDAS )
Multi Objective Optimization in the basis of ratio analysis (MOORA)
Weightage
Analytical hierarchy process ( AHP )
Criteria importance through intercriteria correlation (CRITIC)
ENTROPY

## Slide 8
To select the best battery storage for electric vehicles from alternatives using multi criteria decision making techniques.
OBJECTIVE

## Slide 9: LITERATURE SURVEY
SL.NO | AUTHOR | TITLE OF PAPER | JOURNAL | INFERENCE
1 | Arun et al. (2022) | Review on Li-Ion Battery vs Nickel Metal Hydride Battery in EV. | Advances in Materials Science and Engineering, 2022 | Energy, Voltage comparisons. High discharge rate for NiMH. Low cost for NiMH. No maintenance for Li-Ion, but low maintenance required for NiMH.
2 | Maheshwari et al. (2022) | Modelling and State of Charge Estimation of Li-Ion Battery for Electric Vehicle. | In Power Electronics and High Voltage in Smart Grid (pp. 139-151). Springer, 2022 | Necessitates an accurate state of charge (SOC) estimation technique to control charging and discharging. High power to weight ratio and outstanding high temperature performance. Higher energy density.
3 | Ramkumar et al. (2022) | Review on Li-Ion Battery with Battery Management System in Electrical Vehicle. | Advances in Materials Science and Engineering, 2022. | BEV, HEV and PHEV type of electric vehicles. Electronic components for monitoring EV battery’s. Minimum operating expenses for EV since they have fewer moving components.
EV Batteries.

## Slide 10
SL.NO | AUTHOR | TITLE OF PAPER | JOURNAL | INFERENCE
4 | T V Chian et al. (2019) | A Review on recent progress on batteries for EV’s | International Journal of Applied Engineering Research | The development and revolution of battery technology from old centuries to latest battery technology have been reviewed in the paper.
5 | Norio et al. (2013) | High-power and long-life lithium-ion batteries using lithium titanium oxide anode for automotive and stationary power applications | Journal of Power Sources, Volume 244, 15 December 2013 | Cell performance and electrochemical characteristics of LTO/LMO system and LTO/NCM system were investigated for automotive and stationary applications
EV Batteries Contd.

## Slide 11
SL.NO | AUTHOR | TITLE OF PAPER | JOURNAL | INFERENCE
1 | Anilkumar et al. (2021) | Optimum selection of phase change material for solar box cooker integrated with thermal energy storage unit using multi-criteria decision-making technique | Journal of Energy Storage, 2021 | AHP, ENTROPY, CRITIC method for criteria weightage. TOPSIS, EDAS, MOORA for selection of alternatives based on criteria weightage.
2 | Lee et al. (2018) | Comparative analysis of MCDM methods for ranking renewable energy sources in Taiwan | Renewable and Sustainable Energy Reviews, 2018 | WSN ,TOPSIS,VIKOR,ELECTRE MCDM technique analysis.
3 | Emovon et al. (2020) | Application of MCDM method in material selection for optimal design. | Results in Materials, 7, 100115, 2020 | Cost criterion is most used, best results from hybrid MCDM methods MAUA, WSM, WPM methods
4 | Kumar et al. (2017) | A review of multi criteria decision making (MCDM) towards sustainable renewable energy development. | Renewable and Sustainable Energy Reviews, 2017 | Finding optimum results in complex scenarios. Flexibility in decision making. Most suitable method for solving issues related to energy.
MCDM Techniques

## Slide 12: METHODOLOGY
AHP
Step 1: Developing a hierarchical structure.
Step 2: Determining the relative importance of different attributes.
( Pair wise comparison matrix )
Step 3: Normalizing pair wise comparison matrix.
Step 4: Finding criteria weightage.
Step 5: Finding consistency of obtained criteria weightage.
Equations used in AHP:
Consistency ratio = Consistency Index(C.I)/Random Index(RI)
Random Index ( RI ) Table
where n = number of criteria.
λmax =
n | 1 | 2 | 3 | 4 | 5 | 6
RI | 0.00 | 0.00 | 0.58 | 0.90 | 1.12 | 1.24

## Slide 13
ENTROPY
Step 1: Normalizing decision matrix.
where, m = number of alternatives
Step 2: Compute Entropy.
Step 3: Compute the weight vector.

## Slide 14
CRITIC
Step 1: Normalizing the decision matrix.
Step 2: Calculate the standard deviation for each criteria.
Syntax:- “stdeva“ in excel
Step 3: Determining the symmetric matrix.
Syntax:- “correl” in excel
Step 4: Calculate measure of conflict created by criteria.
Step 5: Determine the quantity of information (Cj)
Step 6: Calculate objective weight.

## Slide 15
TOPSIS
Step 1: Normalizing decision matrix.
Step 2: Weightage normalized decision matrix.
Step 3: Finding ideal best () and worst () values.
Step 4: Finding Euclidean distance from ideal best and worst.
Step 5: Determining Performance score ( for each alternative.

## Slide 16
EDAS
Step 1: Determining the average solution.
Step 2: Calculate the positive distance from average.
Step 3: Calculate the negative distance from average.
Step 4: Weighted sum of PDA.
Step 5: Weighted sum of NDA.
Step 6: Normalize values of SP and SN.
Step 7: Normalize the values of NSN and NSP.

## Slide 17
MOORA
Step 1: Normalize the decision matrix.
Step 2: Estimation of assessment values.

## Slide 18
Alternatives/ Attributes | Specific Energy (Wh/kg) | Energy Density (Wh/L) | Specific Power (W/kg) | Life Cycle | Energy Efficiency (%) | Production Cost | Working Temp (Degree Celcius) | Nominal Voltage/Cell (Volt)
LFP | 120[4] | 220[4] | 3250[4] | 5000[4] | 87.5[4] | 0.335[4] | 80[4] | 3.2[4]
NiMH | 82.5[2] | 200[2] | 250[2] | 3000[2] | 70[2] | 0.335[2] | 45[2] | 1.2[2]
LTO | 90[5] | 177[5] | 4000[5] | 18000[5] | 87.5[5] | 0.665[5] | 60[5] | 2.4[5]
LMO | 125[5] | 125[5] | 110[5] | 750[5] | 95[5] | 0.665[5] | 85[5] | 3.9[5]
LCO | 175[4] | 175[4] | 160[4] | 500[4] | 90[4] | 0.335[4] | 80[4] | 3.7[4]
Ni-Cd | 65[3] | 300[3] | 200[3] | 2000[3] | 75[3] | 0.335[3] | 60[3] | 1.2[3]
ZEBRA | 118[1] | 181[1] | 179[1] | 3000[1] | 80.9[1] | 0.5[1] | 350[1] | 2.58[1]
Decision Matrix
[1] Veneri et al. (2017)
[2] Ovshinsky et al. (1993)
[3] Atmaja et al. (2015)
[4] Sharad et al. (2022)
[5] Norio et al. (2013)

## Slide 19: Results and Discussion
AHP
Attributes | Weightage
Specific Energy | 0.227
Energy Density | 0.157
Specific Power | 0.107
Life Cycle | 0.049
Energy Efficiency | 0.073
Production Cost | 0.023
Working Temp | 0.034
Nominal Voltage/Cell | 0.327
Attributes | Specific Energy | Energy Density | Specific Power | Life Cycle | Energy Efficiency | Production Cost | Working Temp | Nominal Voltage/Cell
Specific Energy | 1 | 2 | 3 | 5 | 4 | 7 | 6 | 0.5
Energy Density | 0.5 | 1 | 2 | 4 | 3 | 6 | 5 | 0.333
Specific Power | 0.333 | 0.5 | 1 | 3 | 2 | 5 | 4 | 0.25
Life Cycle | 0.2 | 0.25 | 0.333 | 1 | 0.5 | 3 | 2 | 0.167
Energy Efficiency | 0.25 | 0.333 | 0.5 | 2 | 1 | 4 | 3 | 0.2
Production Cost | 0.143 | 0.167 | 0.2 | 0.333 | 0.25 | 1 | 0.5 | 0.111
Working Temp | 0.167 | 0.2 | 0.25 | 0.5 | 0.333 | 2 | 1 | 0.143
Nominal Voltage/Cell | 2 | 3 | 4 | 6 | 5 | 9 | 7 | 1
Sum | 4.593 | 7.45 | 11.283 | 21.833 | 16.083 | 37 | 28.5 | 2.704

## Slide 20
AHP-TOPSIS
Alternatives | Si+ | Si- | Pi ( Relative Closeness Values) | Rank
LFP | 0.067 | 0.124 | 0.647 | 1
NiMH | 0.166 | 0.0378 | 0.185 | 7
LTO | 0.098 | 0.112 | 0.532 | 4
LMO | 0.111 | 0.130 | 0.539 | 3
LCO | 0.098 | 0.141 | 0.588 | 2
Ni-Cd | 0.170 | 0.057 | 0.251 | 6
ZEBRA | 0.122 | 0.075 | 0.381 | 5

## Slide 21
AHP-EDAS
Alternatives | Average | Rank
LFP | 0.804 | 2
NiMH | 0.577 | 5
LTO | 0.956 | 1
LMO | 0.487 | 6
LCO | 0.628 | 3
Ni-Cd | 0.580 | 4
ZEBRA | 0.013 | 7
Alternatives | NSPi | NSNi
LFP | 0.608 | 1
NiMH | 0.367 | 0.786
LTO | 1 | 0.912
LMO | 0.220 | 0.754
LCO | 0.436 | 0.821
Ni-Cd | 0.428 | 0.731
ZEBRA | 0.026 | 0

## Slide 22
Alternatives | Assessment Values | Rank
LFP | 0.392 | 1
NiMH | 0.199 | 7
LTO | 0.366 | 3
LMO | 0.319 | 4
LCO | 0.367 | 2
Ni-Cd | 0.212 | 6
ZEBRA | 0.254 | 5
AHP-MOORA

## Slide 23
2. ENTROPY
Attributes | Weightage
Specific Energy | 0.025
Energy Density | 0.020
Specific Power | 0.347
Life Cycle | 0.349
Energy Efficiency | 0.004
Production Cost | 0.031
Working Temp | 0.176
Nominal Voltage/Cell | 0.048
Alternatives/ Attributes | Specific Energy | Energy Density | Specific Power | Life Cycle | Energy Efficiency | Production Cost | Working Temp | Nominal Voltage/Cell
LFP | -0.291 | -0.292 | -0.366 | -0.248 | -0.283 | -0.236 | -0.236 | -0.305
NiMH | -0.237 | -0.279 | -0.106 | -0.220 | -0.253 | -0.236 | -0.166 | -0.179
LTO | -0.249 | -0.263 | -0.349 | -0.325 | -0.283 | -0.327 | -0.198 | -0.267
LMO | -0.294 | -0.216 | -0.269 | -0.086 | -0.294 | -0.327 | -0.244 | -0.329
LCO | -0.335 | -0.261 | -0.075 | -0.063 | -0.287 | -0.236 | -0.236 | -0.323
Ni-Cd | -0.206 | -0.331 | -0.090 | -0.172 | -0.263 | -0.236 | -0.198 | -0.179
ZEBRA | -0.286 | -0.266 | -0.083 | -0.220 | -0.273 | -0.290 | -0.357 | -0.276
Summation Column wise | -1.901 | -1.911 | -1.342 | -1.338 | -1.939 | -1.891 | -1.639 | -1.861
Ej | 0.977 | 0.982 | 0.689 | 0.687 | 0.996 | 0.972 | 0.842 | 0.956
1 - Ej | 0.022 | 0.0179 | 0.310 | 0.312 | 0.003 | 0.027 | 0.157 | 0.0432

## Slide 24
ENTROPY-TOPSIS
Alternatives | Si+ | Si- | Pi ( Relative Closeness Values ) | RANK
LFP | 0.241 | 0.257 | 0.515 | 2
NiMH | 0.370 | 0.145 | 0.282 | 3
LTO | 0.016 | 0.430 | 0.962 | 1
LMO | 0.407 | 0.121 | 0.229 | 6
LCO | 0.408 | 0.123 | 0.232 | 5
Ni-Cd | 0.386 | 0.134 | 0.258 | 4
ZEBRA | 0.397 | 0.046 | 0.105 | 7

## Slide 25
ENTROPY-EDAS
Alternatives | Average | Rank
LFP | 0.691 | 2
NiMH | 0.219 | 3
LTO | 0.934 | 1
LMO | 0.007 | 7
LCO | 0.083 | 6
Ni-Cd | 0.152 | 4
ZEBRA | 0.110 | 5
Alternatives | NSPi | NSNi
LFP | 0.383 | 1
NiMH | 0.039 | 0.399
LTO | 1 | 0.868
LMO | 0.015 | 0
LCO | 0.046 | 0.119
Ni-Cd | 0.041 | 0.263
ZEBRA | 0.007 | 0.219

## Slide 26
ENTROPY-MOORA
Alternatives | Average | Rank
LFP | 0.304 | 2
NiMH | 0.065 | 3
LTO | 0.581 | 1
LMO | 0.008 | 6
LCO | 0.022 | 5
Ni-Cd | 0.039 | 4
ZEBRA | -0.069 | 7

## Slide 27
3. CRITIC
Attributes | Cj | Weightage
Specific Energy | 2.192 | 0.107
Energy Density | 2.512 | 0.122
Specific Power | 2.601 | 0.127
Life Cycle | 2.423 | 0.118
Energy Efficiency | 2.182 | 0.106
Production Cost | 3.723 | 0.181
Working Temp | 2.299 | 0.112
Nominal Voltage/Cell | 2.619 | 0.127
20.5564

## Slide 28
CRITIC-TOPSIS
Alternatives | Si+ | Si- | Pi ( Relative Closeness Values) | RANK
LFP | 0.087 | 0.130 | 0.599 | 2
NiMH | 0.143 | 0.102 | 0.415 | 4
LTO | 0.067 | 0.167 | 0.711 | 1
LMO | 0.156 | 0.092 | 0.371 | 6
LCO | 0.145 | 0.108 | 0.427 | 3
Ni-Cd | 0.148 | 0.104 | 0.412 | 5
ZEBRA | 0.164 | 0.043 | 0.209 | 7

## Slide 29
CRITIC-EDAS
Alternatives | Average | Rank
LFP | 0.759 | 2
NiMH | 0.265 | 4
LTO | 0.892 | 1
LMO | 0.263 | 5
LCO | 0.398 | 3
Ni-Cd | 0.251 | 6
ZEBRA | 0.004 | 7
Alternatives | NSPi | NSNi
LFP | 0.518 | 1
NiMH | 0.148 | 0.382
LTO | 1 | 0.784
LMO | 0.205 | 0.322
LCO | 0.293 | 0.502
Ni-Cd | 0.210 | 0.292
ZEBRA | 0.009 | 0

## Slide 30
CRITIC-MOORA
Alternatives | Assessment Values | Rank
LFP | 0.227 | 2
NiMH | 0.0917 | 5
LTO | 0.249 | 1
LMO | 0.071 | 6
LCO | 0.143 | 3
Ni-Cd | 0.099 | 4
ZEBRA | 0.015 | 7

## Slide 31: Rank Comparison
ALTERNATIVES/ MCDM Methods | AHP-TOPSIS | AHP-EDAS | AHP-MOORA | ENTROPY-TOPSIS | ENTROPY-EDAS | ENTROPY-MOORA | CRITIC-TOPSIS | CRITIC-EDAS | CRITIC-MOORA
LFP | 1 | 2 | 1 | 2 | 2 | 2 | 2 | 2 | 2
NiMH | 7 | 5 | 7 | 3 | 3 | 3 | 4 | 4 | 5
LTO | 4 | 1 | 3 | 1 | 1 | 1 | 1 | 1 | 1
ZEBRA | 5 | 7 | 5 | 7 | 5 | 7 | 7 | 7 | 7
LMO | 3 | 6 | 4 | 6 | 7 | 6 | 6 | 5 | 6
LCO | 2 | 3 | 2 | 5 | 6 | 5 | 3 | 3 | 3
Ni-Cd | 6 | 4 | 6 | 4 | 4 | 4 | 5 | 6 | 4

## Slide 32
Comparison of Optimum results from MCDM technique, using Spearman rank correlation coefficient (rs)
MCDM Methods | AHP-TOPSIS | AHP-EDAS | AHP-MOORA | ENTROPY-TOPSIS | ENTROPY-EDAS | ENTROPY-MOORA | CRITIC-TOPSIS | CRITIC-EDAS | CRITIC-MOORA | AVERAGE
AHP-TOPSIS | 1 | 0.42 | 0.96 | 0.071 | -0.107 | 0.071 | 0.39 | 0.5 | 0.42 | 0.41
AHP-EDAS | 0.42 | 1 | 0.607 | 0.857 | 0.67 | 0.857 | 0.96 | 0.89 | 1 | 0.80
AHP-MOORA | 0.96 | 0.607 | 1 | 0.25 | 0.107 | 0.25 | 0.57 | 0.64 | 0.607 | 0.55
ENTROPY-TOPSIS | 0.071 | 0.857 | 0.25 | 1 | 0.89 | 1 | 0.89 | 0.821 | 0.857 | 0.73
ENTROPY-EDAS | -0.107 | 0.67 | 0.107 | 0.89 | 1 | 0.89 | 0.714 | 0.607 | 0.678 | 0.61
ENTROPY-MOORA | 0.071 | 0.857 | 0.25 | 1 | 0.89 | 1 | 0.89 | 0.821 | 0.857 | 0.74
CRITIC-TOPSIS | 0.39 | 0.96 | 0.57 | 0.89 | 0.714 | 0.89 | 1 | 0.964 | 0.964 | 0.82
CRITIC-EDAS | 0.5 | 0.89 | 0.64 | 0.821 | 0.607 | 0.821 | 0.964 | 1 | 0.892 | 0.79
CRITIC-MOORA | 0.42 | 1 | 0.607 | 0.857 | 0.678 | 0.857 | 0.964 | 0.892 | 1 | 0.81

## Slide 33: CONCLUSION
Optimum selection of batteries are important for EV’s.
Selection done through MCDM techniques like TOPSIS, EDAS, MOORA and criteria weightage through AHP, CRITIC, ENTROPY methods.
AHP-MOORA, AHP-TOPSIS, ENTROPY-EDAS MCDM techniques are ignored as they have low similarity in rankings with other methods.
LTO EV battery is selected as the best from the alternatives.

## Slide 34: References
Anilkumar, B. C., Maniyeri, R., & Anish, S. (2021). Optimum selection of phase change material for solar box cooker integrated with thermal energy storage unit using multi-criteria decision-making technique. Journal of Energy Storage, 40, 102807.
Lee, H. C., & Chang, C. T. (2018). Comparative analysis of MCDM methods for ranking renewable energy sources in Taiwan. Renewable and Sustainable Energy Reviews, 92, 883-896.
Emovon, I., & Oghenenyerovwho, O. S. (2020). Application of MCDM method in material selection for optimal design: A review. Results in Materials, 7, 100115.
Rathod, M. K., & Kanzaria, H. V. (2011). A methodological concept for phase change material selection based on multiple criteria decision analysis with and without fuzzy environment. Materials & Design, 32(6), 3578-3585.
Ovshinsky, S. R., Fetcenko, M. A., & Ross, J. (1993). A nickel metal hydride battery for electric vehicles. Science, 260(5105), 176-181.
Veneri, O., Capasso, C., & Patalano, S. (2017). Experimental study on the performance of a ZEBRA battery based propulsion system for urban commercial vehicles. Applied Energy, 185, 2005-2018.
Atmaja, T. D. (2015). Energy storage system using battery and ultracapacitor on mobile charging station for electric vehicle. Energy Procedia, 68, 429-437.